## Slide 1: Clock Synchronization in Sensor Networks(Distributed Systems)
Ritika Kumari
Vinit Kamboj

## Slide 2
Motivation
Synchronizing time is essential for many applications
  Coordination of wake-up and sleeping times (energy efficiency)
  TDMA schedules
  Ordering of collected sensor data/events
  Co-operation of multiple sensor nodes
  Estimation of position information (e.g. shooter detection)
Goals of clock synchronization
  Compensate offset between clocks
  Compensate drift between clocks
  Agreement in reading two clocks
Time Synchronization
Sensing
Localization
Duty-Cycling
TDMA

## Slide 3: Wireless Sensor Network (WSN)
Network using many wireless sensors
Dropped from a plane to monitor area
  Random placement
Sensors build hierarchical network once deployed

## Slide 4: Network Flooding
Broadcast packet from root node
If packet received for the first time
  Set Parent on Tree = Source of message
  Change Source field to MyId
  Increment HopCount field
  Rebroadcast packet

## Slide 5: Problem with unsynchronized clocks
In distributed banking system, if timing and ordering of financial transactions are not tracked, it may raise inconsistent state in the system.
A distributed online reservation system in which the last available seat may get booked from multiple nodes if their local clocks are not synchronized.
There is a need to transmit a message from one node to another at any time. This will become difficult if sender and receiver clocks are not synchronized with each other.

## Slide 6: Clock Synchronization Problem
Relation between clock time and UTC when clocks ticks at different rates.

## Slide 7: Reasons for Delay in Synchronization
Communication Link Failure
Fault Tolerance
Propagation Time
Non-Receipt of Acknowledgement
The Bandwidth of Communication Link

## Slide 8: Wireless Sensors
Physically small sensing unit
  Battery
  Processor
    Slow
    Drift
  Radio/antenna
  Sensor modules
Covert
Short battery life

## Slide 9: Applications
Temperature
  Fire detection
  Brake usage
Humidity
  Flood detection
Pressure
Object tracking
  Animal movement and migrations
  Vehicle tracking
Noise levels
  Search and rescue efforts
  Locating a sniper’s position
Contamination levels
  Monitoring pollution levels
  Chemical/biological agent detection
Mechanical stress on supporting structures

## Slide 10: Existing Synchronization Solutions
Network Time Protocol (NTP)
  Computationally infeasible for wireless sensors
Reference Broadcast Synchronization (RBS)
  Receiver-receiver synchronization
Timing-sync Protocol for Sensor Networks (TPSN)
  Transmitter-receiver synchronization
Hybrid Synchronization

## Slide 11: Network Time Protocol

## Slide 12: NTP Modes
Multicast:
  One computer periodically multicasts time info to all other computers on network
  These adjust clock assuming a very small transmission delay
  Only suitable for high speed LAN’s; yield’s low but usually acceptable sync.
Procedure-call:
  Server accepts request from clients
  Applicable where higher accuracy is needed ,or where multicast is not supported by the network’s hard-and-software
Symmetric:
  Used where high accuracy is needed.
NTP Basic Idea
Layered client-server architecture, based on UDP message passing
Synchronization at clients with higher strata number less accurate due to increased latency to strata1 time server
Failure robustness: If a strata 1 server fails, it may become a strata 2 server that is being synchronized though another strata 1 server.

## Slide 13: NTP Delay and Offset

## Slide 14: NTP Implementation model

## Slide 15: Reference Broadcast Synchronization
Receiver-to-receiver synchronization
Two stages
  Transmitter broadcasts clock time
  Receivers exchange observations

## Slide 16: RBS Energy Usage
Given n receivers:
Transmissions grow as O(n)
Receptions grow as O(n2)

## Slide 17: Timing-sync Protocol for Sensor Networks
Features
  Sender-receiver bidirectional mechanism
  Two phases of operation:
    Level discovery and synchronization
  Level discovery phase
    Root node initiates level discovery
    A node on receiving its level broadcasts it
    Any node receiving multiple level packets takes the first one and ignores the others
    Any node not receiving a level packet times out and sends a request for level packet

## Slide 18: TPSN Model – Synchronization Phase
Each node (A) broadcasts synchronization_pulse
  Timestamped at T1
Node B receives pulse at T2, broadcasts ack at T3
Node A receives ack at T4
Δ is clock drift
d is propagation delay

## Slide 19: TPSN Energy Usage
Given n receivers:
Transmissions and receptions grow as O(n)
Large energy savings over RBS for large n
Less efficient for small n

## Slide 20: Uncertainties
Sender uncertainty
  RBS removes it completely
  Minimized in TPSN by timestamping at MAC layer
Propagation/receiver uncertainties, and relative local clock drifts
  TPSN outperforms RBS by factor of 2

## Slide 21: Accuracy Comparison
 | TPSN | RBS
Avg error (μs) | 16.9 | 29.1
Worst-case error (μs) | 44 | 93
Best-case error (μs) | 0 | 0
% time error < avg | 64 | 53

## Slide 22: Hybrid Synchronization
Complete system for WSN operation
Three stages
  Build hierarchical tree with flooding
    Transmitters know how many receivers are connected
  Periodically synchronize sensors
  Re-elect new root when current one dies

## Slide 23: Hybrid Synchronization
RBS best for small n, TPSN best for large n
Calculate optimal cutoff value to choose RBS or TPSN algorithm (receiver_threshold)
  Transmissions and receptions draw different current
  where α is reception-to-transmission current ratio

## Slide 24: Hybrid Synchronization Algorithm
If num_receivers < receiver_threshold
  Transmitter broadcasts sync_request
  For each receiver
    Record local time of reception for sync_request
    Broadcast observation_packet
    Receive observation_packet from other receivers
Else
  Transmitter broadcasts sync_request
  For each receiver
    Record local time of reception for sync_request
    Broadcast ack_packet to transmitter with local time
Equate energies of both RBS and TPSN
Solve equation to find receiver_threshold

## Slide 25: Sensor Synchronization Simulations
Verify the hybrid synchronization algorithm works with several sensor architectures
  Run hybrid usRun RBS, TPSN, hybrid using optimal receiver_threshold
  ing non-optimal receiver_threshold values
  Change sensor architecture
Used 500 sensors per network

## Slide 26
Synchronization Simulations for 250 Sensors
Synchronization Simulations for 500 Sensors
Synchronization Simulations for Variable Network Size

## Slide 27
Synchronization Simulations for 750 Sensors
Synchronization Simulations for 1000 Sensors
Synchronization Simulations for Variable Network Size

## Slide 28: Network Size Simulations
Hybrid saves up to 50% over RBS, up to 20% over TPSN
Hybrid is still more efficient in networks favoring either RBS or TPSN
Sensors | 250 | 500 | 750 | 1000
RBS | 446 | 1046 | 1844 | 2762
TPSN | 511 | 983 | 1434 | 1885
Hybrid | 404 | 828 | 1253 | 1672
RBS Savings | 9.29% | 20.79% | 32.04% | 39.46%
TPSN Savings | 20.80% | 15.73% | 12.65% | 11.28%

## Slide 29: Conclusions:
Synchronization is necessary for most sensor networks to operate effectively
Both TPSN and RBS synchronize sensor clocks locate origin of gunshot blast
Neither TPSN nor RBS are designed for low energy usage
Hybrid algorithm adapts to any size network and saves energy over other algorithms

## Slide 30: References
J. Elion, 1. Gird, and D. Estrin, "Fine-Grained Time Synchronization using Reference Broodcaiti,". Proc. 5th Symp. Op. Sys. Design and Implemenfotion, Barton, MA, DR. 2002.
K. Remer, 'Time Synchronization in Ad Hoc Networks," ACM MobiHcx '01, Lon Bwch, CA, Oct. 2001
Bell communications Research, “Digital Synchronization network plan,” Tech. Advisory TA-NPG000436, Nov. 1, 1986.
Defense Advanced Research Projects Agency, Internet Control Message Protocol, DARPA Network Working Group Rep. RFC-792, U.S.C. Inform. Sci. Inst., Sept. 1981.
I.F. Akyildiz, W. Su, Y. Sankarasubramanian, and E. Cayirci. A Survey on Sensor Networks. IEEE Communications Magazine, 40(8):102–114, Aug. 2002.
K. Arvind. Probabilistic Clock Synchronization in Distributed Systems. IEEE Transactions on Parallel and Distributed Systems, 5(5):474–487, May 1994.